## Slide 1: Droplet Generation in a Microfluidic T-Junction
Group - 2
| Gopal - 20CH30008 | Vikram - 20CH10084 |
| Chetan - 20CH10014 | Aryan - 20CH10089 | Sanidhya - 20CH10055 |

## Slide 2: Problem Statement
A 3-D dimensional T–junction microchannel, as shown in figure, is considered to investigate the water droplet formation in a liquid (Oil)
9
4
3
0
(0,0,0)
5
6
2
100µm
1600µm
Properties | Water | Oil
Density | 990 kg/m3 | 859 kg/m3
Viscosity | 2.8 × 10-2 Pa.s | 9.8 × 10-1 Pa.s
Interfacial Tension | 4 × 10-3 N/m | 4 × 10-3 N/m
Inlet Velocity | 0.0083 m/s | 0.0083 m/s
1
250µm
16
19
8
7
200µm
250µm
100µm

## Slide 3: Mesh Creation
The construction of the T-Junction is broken down into 4 blocks
Sections | Dimensions | Color Code
Section 1 (Oil Inlet) | 100 𝜇m × 100 𝜇m × 250 𝜇m | 
Section 2 (Water Inlet) | 100 𝜇m × 100 𝜇m × 250 𝜇m | 
Section 3 (T-Intersection Box) | 100 𝜇m × 100 𝜇m × 100 𝜇m | 
Section 4 (Co-flow Channel) | 100 𝜇m × 100 𝜇m × 1250 𝜇m | 
Grid Size (∆x = ∆y = ∆z) = 10 𝜇m
Block-Mesh
Set-Field (alpha)
Sections | Dimensions | Color Code
Alpha = 0 (Oil) | 100 𝜇m × 100 𝜇m ×1650 𝜇m | 
Alpha = 1 (Water) | 100 𝜇m × 100 𝜇m × 200 𝜇m | 
200 𝜇m

## Slide 4: Boundary Conditions
Block-Mesh (Filename: blockMeshDict)
  Inlets and Outlet - type patch - (No geometry/ topological conditioning)
  Walls - type wall
Velocity (Filename: U)
  Inlet1 - fixedValue (0.0083 0 0) and Inlet2 - fixedValue(0 0.0083 0)
  Outlet - zeroGradient (Value unknown or to be calculated)
  Walls - noSlip (fluid velocity at the wall is zero)
Pressure (Filename: p_rgh)
  Inlet1 and Inlet2 - zeroGradient
  Outlet - fixedValue (0)
  Walls - zeroGradient
Alpha (Filename: alpha_water)
  Inlet1 - fixedValue (0)
  Inlet2 - fixedValue (1)
  Outlet – zeroGradient
  Walls - zeroGradient

## Slide 5: Working Principle behind Solver (interFoam)
interFoam:
‘Solver for 2 incompressible, isothermal immiscible fluid using a VOF (volume of fluid) phase-fraction based interface capturing approach’
Use-cases:
  Incompressible
  transient
  laminar and turbulent
  Multiphase
  Immiscible
  VOF
  Isothermal
Combines the PISO and SIMPLE algorithms to give the PIMPLE algorithm

## Slide 6: Results
0.5 sec
1 sec
4 sec
10 sec
7 sec
14 sec

## Slide 7
Observations
Observed multiphase annular flow in the initial phase, followed by stratified flow for given operating conditions
The turbulence/disturbances observed decreased over time
The time steps observed were extremely small (order of less than 10-5)

## Slide 8
Future Scope in Our Project
In future, prospect we can conduct Grid Independent Test(Efficiency vs Accuracy).
Implement a dynamic mesh adaptation technique which can help in refining the mesh where it is needed, improving the accuracy of your simulations and reducing computational costs.
By varying the velocity, we can Investigate transitional regimes between different flow patterns which can provide valuable information for device design and operation.

## Slide 9: Thank You